## Slide 1
S
P
Legend
Manual, High Integrity On/Off Valve
High Precision Critical Orifice
High Precision Vacuum/Pressure Gauge
Fast, Low Dead Space Solenoid Valve
From
Tower
To
Pump
Sampling
Canister
Closed
Open
P
S
Open
Switching
Smart REA Sampler
Collection Mode
Identical systems for ‘up’ and ‘down’ sampling.
Need to minimize dead volume between solenoid and critical orifice.
Pressure gauge needs to work across wide range… something like <0.1 psi to 30 psi.
Manual valves must be leak tight in vacuum, and solenoid must seal under same conditions.
All tubing & fittings downstream of solenoid are stainless steel.
Filter needed upstream of solenoid (not shown).

## Slide 2
S
P
Legend
Manual, High Integrity On/Off Valve
High Precision Critical Orifice
High Precision Vacuum/Pressure Gauge
Fast, Low Dead Space Solenoid Valve
Sampling
Canister
Open
Open
P
S
Closed
Closed
Smart REA Sampler
Pressurization Mode
After sampling period, canister is filled to ~30 psi with UHP nitrogen.
Pressure gauge records pressure change so that the dilution factor is precisely known.
From
Regulated
Gas Cylinder

## Slide 3
S
P
Legend
Manual, High Integrity On/Off Valve
High Precision Critical Orifice
High Precision Vacuum/Pressure Gauge
Fast, Low Dead Space Solenoid Valve
Sampling
Canister
Open
Open
P
S
Closed
Closed
Smart REA Sampler
Transfer Mode
Pressurized main canister is used to fill several smaller canisters/cartridges.
Cartridges are attached in parallel so that all are filled to same pressure.
Cartridges can be then transferred to laboratory for analysis.
Pressure gauge records pressure change so that the cartridge pressures are known.
Cartridge design still TBD.
To Smaller
Evacuated
Canisters

## Slide 4
S
P
Legend
Manual, High Integrity On/Off Valve
High Precision Critical Orifice
High Precision Vacuum/Pressure Gauge
Fast, Low Dead Space Solenoid Valve
Sampling
Canister
Open
Open
P
S
Open
Closed
Smart REA Sampler
Evacuation Mode
Pump must be able to evacuate system to near vacuum (~0.1 psi or below).
Critical orifice and solenoid also evacuated to minimize contamination.
To Suitable
Vacuum
Pump